## Slide 1: BAND ENGINEERING
이성혁, 전대영, 윤성지, 송승근

## Slide 2
이성혁
전대영
윤성지
송승근

## Slide 3: Band Engineering
1
INTRODUCTION OVERVIEW
이성혁

## Slide 4: Band Engineering
Introduction
Energy Band and Band Gap
1
Energy Bands are composed of energy states
Band gap is an energy range in a solid where no electron states can exist

## Slide 5: Band Engineering
Introduction
Band-gap Engineering
2
process of controlling or altering the band gap of a material
controlling the composition of alloys or constructing layered materials with alternating compositions
Semiconductor Performance spatially varying stoichiometry
Improvement Heterojunction graded band gap
Shockley
1951
Kroemer
1954

## Slide 6: Band Engineering
Introduction
Band-gap Engineering
3
Desired bandgap using epitaxy(homojunction, heterojunction..)
InxAl1-xP

## Slide 7: Band Engineering
Introduction
Band Engineering
4
1D
2D
3D
Band Engineering changing the shape and the curvature of the energy bands

## Slide 8: Band Engineering
Introduction
Why?
5
Possible to make a desired wave length, detection, capability, or desired
Conductance region
Able to increase the electric, thermoelectric efficiency in some cases

## Slide 9: Band Engineering
2
THEORY
전대영

## Slide 10: Band Engineering
Theory
1
Schematic for bandgap engineering of semiconductors. The band structure and optical absorption curves of (a) an intrinsic semiconductor, (b) doping-induced intraband energy states, (c) doping-induced band gap narrowing, and (d) degenerate doping-induced LSPR(localized surface plasmon resonance)

## Slide 11: Band Engineering
Theory
2
r0’
The scale of energy band changes, when r0 moves to r0’

## Slide 12: Band Engineering
Theory
3
When a particle is smaller than bohr radius, the smaller the radius, the larger the band gap. (Bohr radius - distance between the nucleus and the electron in a hydrogen atom in its ground state)

## Slide 13: Band Engineering
Theory
4
Quantum dots (QDs) are tiny semiconductor particles a few nanometres in size, having optical and electronic properties that differ from larger particles due to quantum mechanics.

## Slide 14: Band Engineering
Theory
5
Quantum dots have properties intermediate between bulk semiconductors and discrete atoms or molecules.
Their optoelectronic properties change as a function of both size and shape.
Larger QDs of 5–6 nm diameter emit longer wavelengths, with colors such as orange or red. Smaller QDs (2–3 nm) emit shorter wavelengths, yielding colors like blue and green.
The specific colors vary depending on the exact composition of the QD.

## Slide 15: Band Engineering
3
EXPERIMENTS
윤성지

## Slide 16: Band Engineering
Experiments
⁕ Band engineering in quantum dots
► Changing the Stoichiometric Percentage
: /GaAs quantum dots
- increase of x → lower Γ edge of the conduction band & higher edge of the valence band
1

## Slide 17: Band Engineering
Experiments
⁕ Band engineering in quantum dots
► Changing the Stoichiometric Percentage
: /GaAs quantum dots
- enhancement of indium composition → decrease band gap & electron-hole recombination energy
- The decline is nonlinear and with different slope of band gap and recombination energy.
2

## Slide 18: Band Engineering
Experiments
3
⁕ Band engineering for high-performance thermoelectric materials
1) Manipulating the structure – property relation
- Tuning crystal structures to design pseudocubic structural blocks in non-cubic diamond-like materials
cause cubic-like degenerate valence band → a high thermoelectric figure of merit zT
Max ZT
= 0
= c/2a = 1

## Slide 19: Band Engineering
Experiments
4
⁕ Band engineering for high-performance thermoelectric materials
1) Manipulating the structure – property relation
- Tuning crystal structures to design pseudocubic structural blocks in non-cubic diamond-like materials
cause cubic-like degenerate valence band → a high thermoelectric figure of merit zT

## Slide 20: Band Engineering
Experiments
5
⁕ Band engineering for high-performance thermoelectric materials
2) Using conductive networks in materials
- Doping at voids in skutterudite
PGEC (phonon-glass electron-crystal) → Optimize the electrical and thermal properties
(skutterudite) unit cell
→ Large voids

## Slide 21: Band Engineering
Experiments
6
⁕ Band engineering for high-performance thermoelectric materials
2) Using conductive networks in materials
- Doping at voids in skutterudite
PGEC (phonon-glass electron-crystal) → Optimize the electrical and thermal properties
Filled with impurity atoms
For various n-type filled skutterudites,

## Slide 22: Band Engineering
Experiments
⁕ Band engineering for high-performance thermoelectric materials
3) Transport from spit-orbit-coupling and Rashba effect
- The Rashba effect in materials with strong spin-orbit coupling and inversion asymmetry
→ The degeneracy of spin-up and spin-down bands is lifted.
- DOS is altered across Rashba energy .
- unique DOS → high TE performance
For quantum wells,
For bulk materials,
7

## Slide 23: Band Engineering
4
APPLICATION
송승근

## Slide 24: Band Engineering
Application
1
Band engineering
-Quantum Dot
-Thermoelectric Material
-Strained-Material
Changing Band gap
Changing shape of Band
Light Emitting Diodes (LEDs) Lighting Solar Cells Photodectors Biomedical Imaging
Power generation
Refrigeration
-Graphene

## Slide 25: Quantum Dot
Application
2
QD-LCD vs LCD
QD-LED vs OLED
Higher Color Gamut
Higher Color Gamut
Low power
Lower price
Longer lasting

## Slide 26: Quantum Dot
Application
3
QD-Solarcell
QD-Bio sensor
ADVANTAGE
Lower price
Higher efficiency
DISADVANTAGE
Low stability
Short life resist expectancy
Using as bio marker
Detecting cell
Drug delivery

## Slide 27: Thermoelectric Material
Application
⁕
4
Power generation(Energy Harvesting)

## Slide 28: Thermoelectric Material
Application
⁕
4
PowerWatch
Powered only by body heat
No need to be charged

## Slide 29: Thermoelectric Material
Application
Thermoelectric refrigeration is the process of pumping heat energy out of an insulated chamber in order to reduce the temperature of the chamber below that of the surrounding air. Thermoelectric refrigeration uses a principle called the "PELTIER" effect to pump heat electronically.
5
Thermoelectric Refrigeration
Advantage

## Slide 30
0
Thanks for listening to us :D
End of Presentation

## Slide 31
0
Reference
-Melinda Y. Han,1 Barbaros O¨ zyilmaz,2 Yuanbo Zhang,2 and Philip Kim2 1 Department of Applied Physics and Applied Mathematics, Columbia University, New York, New York 10027, USA 2 Department of Physics, Columbia University, New York, New York 10027, USA (Received 21 February 2007; published 16 May 2007)
-http://electrons.wikidot.com/density-of-states
-https://www.nanosysinc.com/
-https://pid.samsungdisplay.com/ko/learning-center/white-papers/guide-to-understanding-quantum-dot-displays -https://pid.samsungdisplay.com/ko/learning-center/white-papers/quantum-dot-technology
-https://www.sciencedirect.com/science/article/pii/B9780081019771000053
-Mahdi Ahmadi Borj and Esfandiar Rajaei, “Energy Level of Engineering in InGaAs/GaAs Quantum Dots Applicable to QD-Lasers by Changing the Stoichiometric Percentage”, the University of Guilan, Rasht, Iran
-Lili Xi, Jiong Yang, Lihua Wu, Jihui Yang, Wenqing Zhang, “Band engineering and rational design of high-performance thermoelectric materials by first-principles”, Journal of Materiomics Volume 2, Issue 2, 2016
https://www.slideshare.net/ut09/thermoelectric-materials-applications
https://www.flickr.com/photos/oregonstateuniversity/6152696629
https://brunch.co.kr/@gungs/78
https://www.koolatron.com/US/en/thermoelectric-refrigeration
https://blog.lgdisplay.com/2017/01/%EC%A7%84%EC%A0%95%ED%95%9C-%ED%94%84%EB%A6%AC%EB%AF%B8%EC%97%84-tv%EB%8A%94-oled%EC%99%80-qled-qd-lcd-%EB%B0%94%EB%A1%9C-%EC%95%8C%EA%B8%B0/